## Slide 1
The Revit MEP API
Jeremy Tammik
Principal Developer Consultant

## Slide 2: About the Presenter
Jeremy Tammik
Principal Developer Consultant
Developer Technical Services
EMEA, Autodesk SARL
  Jeremy is a member of the AEC workgroup of the Autodesk Developer Network ADN team, providing developer support, training, conference presentations, and blogging on the Revit API.
  He joined Autodesk in 1988 as the technology evangelist responsible for European developer support to lecture, consult, and support AutoCAD application developers in Europe, the U.S., Australia, and Africa. He was a co-founder of ADGE, the AutoCAD Developer Group Europe, and a prolific author on AutoCAD application development. He left Autodesk in 1994 to work as an HVAC application developer, and then rejoined the company in 2005.
  Jeremy graduated in mathematics and physics in Germany, worked as a teacher and translator, then as a C++ programmer on early GUI and multitasking projects. He is fluent in six European languages, vegetarian, has four kids, plays the flute, likes reading, travelling, theatre improvisation, yoga, carpentry, loves mountains, oceans, sports, dancing, and especially climbing.
Notes: Before we jump into the presentation proper, here’s a little bit about me. My name is Jeremy Tammik, and I work for the Autodesk Developer Network (ADN), in the AEC workgroup. I also write a blog on the Revit API. I have been working with AutoCAD APIs for over twenty years. A key part of my job is to support communication between external plug-in developers and our engineering to help the latter create the APIs that the former need to write really cool add-in applications.

## Slide 3: Class Summary
Overview of the Revit MEP API
MEP API enhancements in Revit 2013 and 2014
Working programmatically with Revit MEP models
Overview of available Revit MEP API samples
Prerequisites: we assume prior knowledge of
  How to program in .NET
  The basics of the generic Revit API
  Revit MEP product usage

## Slide 4: Learning Objectives
At the end of this class, you will be able to:
Understand and use the latest Revit MEP API enhancements
Analyze, create, manage and modify electrical, HVAC and plumbing models, systems, and components programmatically
Understand and reuse functionality provided by the standard Revit MEP SDK and custom ADN samples

## Slide 5: Agenda
Introduction
Analysis
Hierarchical systems and connectors
Electrical
HVAC and plumbing
API news in Revit MEP 2013 and 2014
Sample applications
Learning more

## Slide 6: Introduction

## Slide 7: Autodesk Developer Network
Access to almost all Autodesk software and SDK’s
  Includes early access to beta software
Members-only website with thousands of technical articles
Product direction through conferences
Unlimited technical support
API training classes
  One to three free for professional members
Marketing benefits
  Exposure on autodesk.com
  Promotional opportunities
www.autodesk.com/joinadn
Notes: Some of you may be unfamiliar with ADN. The Autodesk Developer Network is a program providing professional support to programmers writing add-in applications for Autodesk software. If you think the program benefits listed here would be useful to you, then visit this URL and read more about it. You don’t have to be a commercial software developer to join ADN.

## Slide 8: Acronyms
  ADN Autodesk Developer Network
  AEC Architecture, Engineering, Construction
  API Application Programming Interface
  BIM Building Information Model
  GUI Graphical User Interface
  HVAC Heating, Ventilation, and Air Conditioning
  MEP Mechanical, Electrical, and Plumbing
  RAC Revit Architecture
  RME Revit MEP
  RST Revit Structure
  SDK Software Development Kit
  UI User Interface

## Slide 9: MEP Application Requirements
Mechanical, electrical and plumbing domains
M is for HVAC, i.e. heating, ventilation and air conditioning
Model analysis tools
  Physical, thermal, environmental etc.
  Building codes and regulations
  Geometrical relationships
  MEP project information
  Green Building XML, gbXML
  Spaces and zones
BIM component and data access
  Systems, components, properties and parameters
  Creation and modification
  Traversal and analysis

## Slide 10: The Generic Revit API
Basic Revit API is generic
All flavours use the same Revit API .NET assemblies
Specific additional features exist for each flavour, e.g.
  Room-related functionality in Revit Architecture
  Access to the analytical model in Revit Structure
  Access to the MEP model in Revit MEP
  Onebox supports all in one box
Runtime discipline switching
  ProductType Architecture, Structure, MEP, Revit

## Slide 11: Revit MEP API Evolution
Generic element and parameter access can always be used
Revit 2008 provided no MEP-specific API
Revit 2009 introduced MEP-specific API support
  MEP model, space and zone, equipment, connector, electrical system
Revit MEP 2010 – mechanical
  MEP namespace, support for HVAC and piping systems
Revit MEP 2011 – electrical
  Conduit, cable tray, panel schedule
Revit MEP 2012 – mechanical
  Pipe settings and sizes, placeholder elements, insulation and lining
Revit MEP 2013 – mechanical and analysis
  Routing preferences, analysis and calculation enhancements
Revit MEP 2014 – analysis
  Externalised calculations, CSV parameter replacement, new settings, creation and property enhancements

## Slide 12: Analysis

## Slide 13: MEP Project Info and EnergyDataSettings
EnergyDataSettings object represents gbXML project info
  Manage > Project Settings > Project Information > Energy Data
  Access via EnergyDataSettings.GetFromDocument method
  Define settings for gbXML export, heating and cooling load calculations, conceptual energy analysis
For project location use Document.ActiveProjectLocation
Green Building XML export
        Document.Export(
        string folder,
        string name,
        GBXMLExportOptions );

## Slide 14: Spaces and Zones
Architectural rooms are unsuitable for MEP analysis
  Wrong height, often too large for analysed region
MEP uses space instead of room, and zone to manage spaces
Rooms can be subdivided into exterior and interior subspaces
AddSpaceAndZone SDK sample
  Programmatic creation and management of spaces and zones
FamilyInstance class has Room and Space properties
        FamilyInstance fi; // get a family instance
        Space space = fi.Space; // query space containing it
        Space space2 = fi.get_Space( phase ); // space in a specific phase

## Slide 15: Model Inspection Utilities
Determine component location, space adjacency analysis, etc.
Volumes, rooms and spaces
  FamilyInstance.Space determines space containing family instance
  Room.IsPointInRoom determines if a point is in a room volume
  Space.IsPointInSpace determines if a point is in a space volume
  GetRoomAtPoint and GetSpaceAtPoint return room or space containing point
Element filters by intersection, Boolean operations, etc.
  BoundingBoxIntersectsFilter, BoundingBoxIsInsideFilter, BoundingBoxContainsPointFilter, ElementIntersectsElementFilter, ElementIntersectsSolidFilter
Ray intersection
  ReferenceIntersector class, ex FindReferencesWithContextByDirection method
  Shoot a ray through the model, given a starting point and direction vector
  Return an array of references of intersected elements and faces
  AvoidObstruction, FindColumns, MeasureHeight, RayTraceBounce SDK samples

## Slide 16: ReferenceIntersector Class
Constructor specifies target elements, target type and 3D view
Elements specified by ElementId, ElementIdSet , ElementFilter
Target type can be elements, meshes, edges, curves, faces
        ReferenceIntersector( <elements>, FindReferenceTarget, View3d )
Call Find or FindNearest to cast a ray given origin and direction
Returns references intersecting ray, or closest to origin
        Find( XYZ origin, XYZ direction )
        FindNearest( XYZ origin, XYZ direction )

## Slide 17: Conceptual Energy Analysis API
Energy analysis on conceptual design models
New overload of Document.Export method taking MassGBXMLExportOptions argument
Create a gbXML file containing energy analysis elements generated from conceptual mass family instances
Notes: New classes in the Autodesk.Revit.DB.Analysis namespace provide access to the elements and objects created by Revit to perform energy analysis on conceptual design models. The method Document Export method overload taking a MassGBXMLExportOptions argument exports a gbXML file containing conceptual energy analysis elements (mass elements) only.

## Slide 18: Detailed Energy Analysis Model API
Produce analytical thermal model from physical building model
Retrieve energy analysis detail model and present as tree view
Access Export to gbXML, Heating and Cooling Loads data
Analytical thermal model
  Composed of volumetric elements: spaces, zones, planar surfaces
  Created and initialised by calling EnergyAnalysisDetailModel.Create()
  Methods GetAnalyticalSpaces, Surfaces, Openings, ShadingSurfaces
SDK sample Analysis > EnergyAnalysisModel
Notes: Open
C:\a\lib\revit\2020\SDK\Samples\GeometryAPI\EnergyAnalysisModel\EnergyAnalysisModel.rvt
C:\a\doc\revit\au\2020\sample\Urban House MEP - 2012.rvt
Run RvtSamples > Analysis > EnergyAnalysisModel.
EnergyAnalysisDetailModelTier specifies level of computation detail for energy analysis model.
This new API provides access to the contents of a project's detailed energy analysis model, as seen in the Export to gbXML and the Heating and Cooling Loads features.
This analysis produces an analytical thermal model from the physical model of a building. The analytical thermal model is composed of spaces, zones and planar surfaces that represent the actual volumetric elements of the building.
New classes in Autodesk.Revit.DB.Analysis namespace for the energy analysis detail model itself, creation options, openings, spaces, surfaces and loops can be used to generate and analyze the contents of the detailed energy analysis model. The EnergyAnalysisDetailModel Create method creates and populates the model with appropriate options selected. The methods GetAnalyticalSpace, GetAnalyticalSurfaces, GetAnalyticalOpenings and GetAnalyticalShadingSurfaces extract entities from the analysis model. The method Destroy cleans up the Revit database after finishing with the analysis results.

## Slide 19: Hierarchical Systems and Connectors

## Slide 20: Hierarchical System Structure and MEP Model
MEP systems consist of hierarchically connected components
Many components are represented using family instances
Connectors can link neighbouring components and transfer info
Top level node is MEP system
  Represented by MEPSystem class, with derived classes ElectricalSystem, MechanicalSystem, PipingSystem
Family instance provides MEPModel property
  MEPModel has ConnectorManager and ElectricalSystems properties
  Derived classes include ElectricalEquipment, LightingDevice, LightingFixture, MechanicalEquipment, MechanicalFitting

## Slide 21: Connectors
Connector class
  Used to represent connections in the Revit BIM project context
  Part of MEP component, not independent Revit database element
Logical connectors
  Used in electrical domain
  Cables and wires are possibly not specified
  Enables traversal of connected electrical system hierarchies
Physical connectors
  Connect neighbouring components physically
  Transmit sizing dimensions and flow information
Family editor connection elements
  Independent elements for defining connectors
  Used to model library parts in family context
  Specialised derived classes for duct, pipe and electrical connectors

## Slide 22: Electrical

## Slide 23: Electrical System Hierarchy
Three-tier recursive hierarchy, cf. electrical system browser
Panel > systems or circuits > circuit elements, may be panels
Logical connections between components
Wires are annotation elements
System can be traversed through connectors
Connectivity information also available in element parameters
Electrical samples
  PowerCircuit SDK sample shows creation and editing power circuits
  PanelSchedule SDK demonstrates use of the electrical panel schedule API
  AdnRme electrical sample demonstrates traversal using both MEP connectors and generic parameters (much harder)

## Slide 24: HVAC and Plumbing

## Slide 25: HVAC and Piping Hierarchy
Systems manage the top level system properties
Ducts and pipes define the main flow elements
Fittings implement bends and branches in the system
Connectors hook up the ducts, pipes and fittings

## Slide 26: Systems
MechanicalSystem and PipingSystem classes
Access to equipment, connectors and system type
Access to system properties such as flow and static pressure
DuctNetwork and PipeNetwork properties access system contents
  Ducts and fitting elements in no particular order
  Does not include terminals or equipments
Query connector managers for traversal in flow direction
TraverseSystem SDK sample

## Slide 27: Duct and Pipes
Represented by Duct, FlexDuct, Pipe and FlexPipe classes
  Derived from MEPCurve
Provide read access to duct properties, types, and geometry
Change duct or pipe type
Move duct or pipe
  Use Move method rather than Location
Layout duct or pipe
  Driven by two points, point and connector, or two connectors

## Slide 28: Fittings
Represented by standard RFA family instances
Created using dedicated creation doc New*Fitting methods
Elbow, Tee, Cross, Takeoff, Transition, and Union
Access fitting properties, shape and dimensions through the FamilyInstance.MEPModel property

## Slide 29: Connectors
Read duct, pipe, and fitting connector properties
  Flow, Coefficient, Demand
Access physical connector properties
  Origin, Angle, Height, Width, Radius
Read and write assigned connector properties
The fitting connectors define the properties
  Flow, Flow Configuration, Coefficients, Loss Method
Change connector size and location
Connect and disconnect

## Slide 30: Element Creation
Methods on Autodesk.Revit.Creation.Document
Create New Systems
  NewMechanicalSystem, NewPipingSystem
Create New Elements
  NewFlexDuct, NewFlexPipe
Create New Fittings
  New...Fitting for Cross, Elbow, TakeOff, TeeFitting, Transition, Union
New classes Conduit, CableTray provide static Create methods
Connector elements
  Created in the family context using methods on FamilyItemFactory
  Accessed through the Document.FamilyCreate property
  NewDuctConnector, NewPipeConnector, NewElectricalConnector

## Slide 31: Recent Revit MEP API Enhancements

## Slide 32: Revit MEP 2011 Product Enhancements
Panel Schedules
Cable Tray and Conduit
Other Enhancements
  Placing Valves and Fittings in Section or Elevation Views
  Tagging of MEP Elements during placement
  Demand Factors and Load Categories
  Piping Companion Flanges
  New Electrical Content
  Oval Duct
Notes: Cable Tray and Conduit
Revit 2011 includes support for modelling conduit and cable tray as unique object types. The goal of this feature is to represent real world conduit and cable tray for coordination purposes and for accurate and legible construction drawings.
Cable trays and conduits and can be routed as individual runs with or without individual fittings placed between straight sections. Conduit runs without fittings would be used for conduit that is bent to change directions instead of having actual fittings. When using conduit or cable tray runs without fittings, you can now use a new schedule type to report the overall length of the run. These schedule types have categories of Conduit Runs and Cable Tray Runs respectively.
Cable trays can be drawn as channel or ladder type.
Conduits can be connected to cable tray segments. The conduit does not have to actually touch the cable tray to connect. For example, you can connect a conduit 6” below the cable tray and have the conduit end update if the cable tray segment is moved.
Conduit and cable tray each support graphics with varying levels of detail in fine, medium, and coarse display.
A new type of connector is now available for connecting conduit to equipment. This new surface connector enables an entire face of a piece of equipment to accept conduit connections without having to manually add individual conduit connectors to the equipment. This makes connecting to equipment such as switchgear, transformers and panels faster and easier.
Panel Schedules
You can create a schedule that lists the circuits connected to a panel, and displays information about each circuit such as location on the panel, circuit name, apparent loads, etc. Panel schedules display three main information sections: a header, circuit table, and a loads summary. A new Panel Schedule view for the selected panel is displayed in the drawing area, and panel schedules are added to the project browser under the Panel Schedules folder. A panel schedule shows the following data:
Panel Name
Distribution System supported by the panel
Number of phases available from the panel
Number of wires specified for the distribution system assigned to this panel
Rating of the mains feeding the panel
Type of mounting (Surface or Recessed)
Type of case enclosing the panel
Room where the panel is installed
Name assigned to a load circuit
Rated trip current for a circuit breaker
Number of poles on the circuit breaker
Circuit number
Phases
Apparent load (VA) for each of the phases
Total apparent load for all three phases
Manufacturer
Notation of any changes made to the panel
Root Means Square amperage
Additional circuit and panel information to display can be specified in the panel schedule templates.
Other Enhancements
Placing Valves and Fittings in Section or Elevation Views
It is now possible to place valves, fittings, and other types of duct or piping accessories while in an elevation or section view. For example, you can switch to an elevation view and place a valve in a vertical pipe.
Tagging of MEP Elements during placement
You can now tag MEP components as they are being placed instead of doing so in a separate step.
Piping Companion Flanges
There is a new pipe fitting type for flanges. If you define a flanged pipe type, you can edit the type and specify a companion flange that will be automatically inserted between the pipes and flanged fittings and on connections to equipment like pumps.
Oval Duct
Oval ducts are now available in addition to the rectangular and round duct shapes. New size separators are available for oval duct size annotations and oval ducts can be used in duct sizing.
Demand Factors and Load Categories
Demand factors have been updated to allow for more control over how demand loads are calculated and can be customized. Load categories are customizable and can be displayed in panel schedules.
New Electrical Content
Many new types of electrical content have been added. New content is provided for communications, fire safety, data, nurse call, etc. Control panels have been added in addition to the individual controls or devices, so several of these objects can be connected to their appropriate panels.

## Slide 33: Revit MEP 2011 API Enhancements
New classes for cable tray and conduit
  Pipe to conduit converter sample
Panel schedules
  API access and PanelSchedule SDK sample
Other Enhancements
  EnergyDataSettings
  Validation in ElectricalSystem Properties
  WireMaterialType, InsulationType, TemperatureRatingType
  DuctConnector, PipeConnector, ElectricalConnector
  Demand Factor and Load Classifications
Notes: The Revit MEP API
Many of the enhancements to the Revit 2011 MEP specific API are related to the electrical domain, since the HVAC and mechanical domains were a primary focus of the previous Revit 2010 release. Paralleling the product features, the cable tray, conduit and panel schedules are the main areas of enhancement. A number of other topics have been addressed as well.
Cable Tray and Conduit
The entire new cable tray and conduit feature is fully exposed through the API. Whatever can be done in the user interface should be possible using the API as well. A number of new classes and elements related to the cable tray and conduit ones have been added. The major ones are:
CableTrayConduitBase – the base class for cable trays and conduits.
CableTrayConduitRunBase – the base class for cable tray and conduit runs.
CableTray – a cable tray instance.
CableTrayType – a cable tray type.
CableTrayRun – a cable tray run.
Conduit – a conduit instance.
ConduitType – a conduit type.
ConduitRun – a conduit run.
As a result of the introduction of these new conduit elements, the previously existing classes ConduitType and ConduitTypeSet have been renamed to WireConduitType and WireConduitTypeSet.
Panel Schedules
A new comprehensive API has been introduced to support access to panel schedules and their contents. The major classes exposed by this API are:
TableView – represents a view that shows a table.
TableData – holds most of the data describing the table row, column, and cells.
TableSectionData – holds row, column and cell data for a TableData instance.
PanelScheduleView – represents a view that shows a panel schedule.
PanelScheduleData – holds most of the data that describe the layout, appearance, and style of the rows, columns, and cells of a panel schedule.
PanelScheduleTemplate – represents a branch panel, a switchboard or a data panel template.
PanelScheduleSheetSegment – represents a segment of a panel schedule sheet instance.
PanelScheduleSheetInstance – represents an instance of a panel schedule placed on sheet.
Other Enhancements
EnergyDataSettings
For greater clarity, the gbXMLParamElem class has been renamed to EnergyDataSettings, and some of its members were renamed as well.
Validation in ElectricalSystem Properties
The ElectricalSystem properties Length and VoltageDrop now throw an InvalidOperationException when the value cannot be computed, instead of returning zero.
WireMaterialType, InsulationType, TemperatureRatingType
These classes now inherit from ElementType.
DuctConnector, PipeConnector, ElectricalConnector
These classes now inherit from a new common ConnectorElement base class.
Demand Factor and Load Classifications
The ElectricalSystem LoadClassification property has been replaced with a new property LoadClassifications. It returns a semicolon-delimited string listing the load classifications assigned to the system. Load classifications are now elements and can be found through regular element iteration.
The class DemandFactor was replaced by ElectricalDemandFactorDefinition.
The ElectricalSetting method GetDemandFactor has been replaced by the DemandFactorId property on the ElectricalLoadClassification class, which returns the id of the ElectricalDemandFactorDefinition element assigned to the load classification.

## Slide 34: Revit MEP 2012 Product Features
Placeholder elements
Insulation and lining
Parallel pipe and conduit runs
Sloped piping enhancements: settings, tooltips, connection
System browser filtering, hovering and selection
System: graphic overrides and warnings, disconnect markers, materials, calculation control, connector labels

## Slide 35: Revit MEP 2012 API Enhancements
Pipe settings and sizes
Placeholder ducts and pipes
Duct and pipe insulation and lining
Small Enhancements and Changes
MEP related APIs
  Detailed Energy Analysis
  Conceptual Energy Analysis
Notes: A group of new classes provide read and write access to the MEP pipe settings.
The Duct and Pipe classes provide new methods to create placeholder elements and predicate properties to identify such elements.
New utility methods MechanicalUtils.ConvertDuctPlaceholders and PlumbingUtils.ConvertPipePlaceholdersMechanicalUtils convert a set of placeholder ducts and pipes to real 3D elements.
The new classes DuctInsulation, PipeInsulation, DuctLining and related types support read/write and create access to duct & pipe insulation and lining. In Revit 2012, these objects are now accessible as standalone elements related to their parent duct, pipe, or fitting.

## Slide 36: Placeholder Ducts and Pipes
Placeholder elements indicate a planned layout
System layout can be defined with minimal info and maximum flexibility
Convert into true duct and pipe elements later on
Size, slope and other properties can be assigned
MepPlaceholder sample
  Two commands: CreatePlaceholders and ConvertPlaceholders

## Slide 37: Insulation and Lining
Before, family defined insulation and lining, triplicating geometry
Now insulation and lining can be added programmatically
New classes DuctInsulation, PipeInsulation, DuctLining
Applicable to duct, pipe, and fitting
Support read, write and create access
Accessible as standalone element related to parent
Sample command: InsulateDuctwork
Notes: The new classes DuctInsulation, PipeInsulation, DuctLining and related types support read/write and create access to duct and pipe insulation and lining. In Revit 2012, these objects are accessible as standalone elements related to their parent duct, pipe, or fitting.

## Slide 38: Pipe Settings and Sizes
MEP pipe settings and pipe size settings are now accessible programmatically
Read and write access
Static methods PipeSettings.GetPipeSettings and PipeSizeSettings.GetPipeSizeSettings return singleton objects
Sample command: GetPipeSettings

## Slide 39: Small Enhancements and Changes
Spare and space circuits
  ElectricalSystem.CircuitType property identifies type: circuit, spare or space
  ElectricalSystem.AddToCircuit throws exception on spare or space systems
Cable tray and conduit domain
  Autodesk.Revit.DB.Domain enumeration cable tray and conduit values
Connector
  New read-only properties added for JointType, GenderType and EngagementLength
MEPSystem
  New property MEPSystem.IsEmpty
Graphical warnings for disconnects
  New ‘show graphical warning’ properties and setters on the Application class
Space properties
  BaseHeatLoadOn indicates if heat gain per person properties have default or user defined value
Fitting methods
  New fitting methods no longer remove unused or dangling curve connectors

## Slide 40: Revit MEP 2013 Product Features
Routing preferences
MEP centrelines
MEP properties
Calculation functionality
Enhanced analysis and simulation functionality
Notes: In Revit MEP 2012, you can only define one single default elbow, tee, etc., which is rather limiting. In Revit 2013, however, numerous different setting for different materials and sizes are supported. One of the major MEP API additions provides access to the routing preferences, as demonstrated by the new Routing Preference Analysis SDK sample. Enhancements include programmatic selection of pipe sizes, materials, fitting types, calculation of pipe and duct friction factors, better handling of duct and pipe sections with the new MEPSection base class, handling of viscosity and density at specified temperatures, read and write access to spare circuit values, and retrieval of the localised user-visible display strings for enumeration values.
New physical properties include a new class ThermalProperties, an additional structural material element, structural and thermal material assets that can be shared, and the ability to indicate if thermal information is included in the gbXML export.

## Slide 41: Revit MEP 2013 API Enhancements
Routing preferences
  RoutingPreferenceTools SDK sample
Analysis enhancements
  MEPSection class
  Viscosity and density
  Spare circuit values
  Display strings
  Thermal properties, material assets, and gbXML export
External Services framework
  Wrap external service functionality, enable encapsulation, replacement
  Basis for future MEP calculations and structural code checking
  In place and fully functional, but not yet used, so no examples
Notes: In Revit MEP 2012, you can only define one single default elbow, tee, etc., which is rather limiting. In Revit 2013, numerous different setting for different materials and sizes are supported. One of the major MEP API additions provides access to the routing preferences, as demonstrated by the new Routing Preference Analysis SDK sample. Enhancements include programmatic selection of pipe sizes, materials, fitting types, calculation of pipe and duct friction factors, better handling of duct and pipe sections with the new MEPSection base class, handling of viscosity and density at specified temperatures, read and write access to spare circuit values, and retrieval of the localised user-visible display strings for enumeration values.
New physical properties include a new class ThermalProperties, an additional structural material element, structural and thermal material assets that can be shared, and the ability to indicate if thermal information is included in the gbXML export.

## Slide 42: Analysis, Simulation and Revit MEP API News
Routing preferences: pipe sizes, materials, fitting types
RoutingPreferenceTools SDK sample
Pipe and duct friction factors
MEPSection base class for duct and pipe sections
Viscosity and density, FluidType and FluidTemperature classes
Access to panel schedule spare circuit values
More LabelUtils access to localized user-visible display strings
ConnectorProfileType and PartType enumeration changes
ConnectorElement changes and new static creation methods
ThermalProperties, thermal material assets, gbXML thermal information
AVF support for deformed shapes
New external services framework
New Light and Light Group API
ReferenceIntersector class
Notes: Let's look at some of the topics going beyond the recorded DevDays Online presentation, starting with some of the new analysis and simulation features.
In Revit MEP 2012, you can only define one single default elbow, tee, etc., which is rather limiting. In Autodesk Revit 2013 software, numerous different setting for different materials and sizes are supported. One of the major MEP API additions provides access to the routing preferences, as demonstrated by the new Routing Preference Analysis SDK sample. Other enhancements enable programmatic selection of pipe sizes, materials, fitting types, calculation of pipe and duct friction factors, better handling of duct and pipe sections with the new MEPSection base class, handling of viscosity and density at specified temperatures, read and write access to spare circuit values, and retrieval of the localized user-visible display strings for enumeration values.
New physical properties include a new class ThermalProperties, an additional structural material element, structural and thermal material assets that can be shared, and the ability to indicate if thermal information is included in the gbXML export.
The structural analytical model includes a new AnalyticalLink element type that can be user defined or automatically generated between two analytical elements and access to link properties like "fixity state".
The Analysis Visualization Framework AVF now better supports the structural analysis workflow, e.g. by including support for deformed shapes.
A Light and Light Group API provides new classes to get and set photometric data, including initial color and intensity, loss factor, color filter and dimming color.
The new ReferenceIntersector class mentioned above provides simplified and more performant ray-cast selection of elements using a given point and direction, similar to the existing FindReferencesWithContextByDirection method, with additional support for filtering the output, e.g. to collect elements, meshes, edges, curves, and faces.

## Slide 43: Revit MEP 2014 API Enhancements
Externalised calculations using external services
ConnectorElement creation methods and properties
Electrical load classification label properties
Fitting parameters CSV replacement
Fitting angle usage settings
DuctSettings class
Curve creation with type id
Connect air terminal directly to duct
Cable tray 'up' direction
Routing preference rule type for caps
Automatic caps on all open connections

## Slide 44: Sample Applications

## Slide 45: Sample Overview
Revit SDK Samples
  AddSpaceAndZone
  AutoRoute
  AvoidObstruction
  CreateAirHandler
  EnergyAnalysisModel
  PanelSchedule
  PowerCircuit
  RoutingPreferenceTools
  TraverseSystem
AdnRme
  Electrical System Hierarchy
  HVAC Air Terminal Sizing
Blog
  Pipe to Conduit Converter
  Cable Tray Creation and Layout
  Loose Connector Navigator
  MEP Placeholders

## Slide 46: AddSpaceAndZone
Retrieve and list existing spaces and zones
  Demonstrates use of an element filter
Create new spaces
  For each closed wall loop or space separation
  Demonstrates use of the NewSpaces method
Create a new zone element
  Specified level and phase
Add and remove spaces in a zone
  Use the AddSpaces and Remove methods

## Slide 47: AutoRoute
Automatically create and route a set of ducts and fittings
  Source is the air supply equipment
  Sink is two air outlet terminals
  Positions can be freely moved
Create a new mechanical system, ducts, fittings and connections
  NewMechanicalSystem, NewDuct, NewElbowFitting, NewTeeFitting and Connector.ConnectTo
  Determine the bounding box of all the three elements
  Use the middle line or quarter lines on the X and Y axes
  Uses.NET framework Trace class to create a log file

## Slide 48: AvoidObstruction
Detect and resolve obstructions between ducts, pipes, and beams
FindReferencesWithContextByDirection ray casting intersection analysis
Split pipe into segments and insert elbows to reroute detour
Resolve collisions between pipes and beams, ducts, and other pipes

## Slide 49: CreateAirHandler
Create an air handler with pipe and duct connectors
Check family category to verify valid mechanical equipment starting point
Use FamilyItemFactory class methods
  NewExtrusion, NewPipeConnector, NewDuctConnector
Set proper connector parameters
Use Document.CombineElements to join the extrusions
Geometric shape creation is generic
Addition of the connectors is MEP specific
Runs in all flavours of Revit

## Slide 50: EnergyAnalysisModel
Retrieve energy analysis detail model and present as tree view
Analytical thermal model generated from physical building model
Similar to Export to gbXML and Heating and Cooling Loads
Analytical thermal model is composed of spaces, zones, planar surfaces
  Volumetric elements
  Created and initialised by calling EnergyAnalysisDetailModel.Create()
  Methods GetAnalyticalSpaces, Surfaces, Openings, ShadingSurfaces

## Slide 51: PanelSchedule
Data exchange sample showing use of the Panel Schedule API
PanelScheduleExport read + export panel schedule CSV or HTML
InstanceViewCreation create panel schedule view instance
SheetImport place all panel schedule views on a sheet
Notes: PanelSchedule: shows how to use the Revit MEP Panel Schedule API:
1. PanelScheduleExport - gets the panel schedule view data via the API and generate a CSV file or a HTML page from it.
2. InstanceViewCreation - Create a panel schedule view instance for an electrical panel you selected.
3. SheetImport - Place the panel schedule view(s) on a sheet view.

## Slide 52: PowerCircuit
  Operate power circuits, similar to legacy RME Circuit Editor toolbar
    Show use of MEPModel and ElectricalSystem classes
    Demonstrate handling interactive element selection
    Implement toolbar user interface for external command
    Use .NET ResourceManager class for image and string resources
  Create a new power circuit with selected elements
  Edit circuit and add and remove circuit elements
  Select or disconnect a circuit panel

## Slide 53: RoutingPreferenceTools
Routing preference analysis and reporting
  Analyse routing preferences of a given pipe type
  Check for common problems
  Look at all rules and criteria for a given pipe type
Routing preference builder XML import and export
  CommandReadPreferences and CommandWritePreferences
  Set pipe type, fitting, and routing preferences in a project
  Export for archival, documentation, and collaboration purposes
  Enable users to work with RP data in a shareable XML format
  Suitable for reuse in a wide variety of BIM management environments

## Slide 54: TraverseSystem
Traverse a mechanical or piping system in the direction of flow
  Check MechanicalSystem IsWellConnected property
Dump the traversal results into an XML file
Determine system
Query base equipment as starting point
Query connector manager for connected neighbour elements
Similar approach works for electrical as well, cf. AdnRme sample

## Slide 55: AdnRme Sample
Non-SDK sample, included in presentation material
HVAC air terminal analysis and sizing
Hierarchical display of an electrical system
Implements a ribbon panel, about box, and progress bar

## Slide 56: AdnRme Electrical Sample
Traverse the electrical system
Reproduce the system browser data structure in a tree view
Display the complete connection hierarchy in a tree view
CmdElectricalConnectors is similar to TraverseSystem SDK sample for ducts
Traversal is also possible using parameter data instead of connector manager, but harder

## Slide 57: AdnRme HVAC Sample
HVAC Task
  Place and size air ducts and terminals
  Analysis and verification of results
Commands aligned with HVAC engineering workflow
  Assign flow to terminals
  Change air terminal size
  Verify design by air flow per surface area
  Reset demo
All modification uses generic parameter and type access
Changes are reflected by schedules and colour fill

## Slide 58: Pipe to Conduit Converter
Two hundred lines of code
My First Revit 2020 Add-in
Illustrates all major Revit 2020 API renovations
  Revit API assembly split
  Namespace reorganisation
  Command registration manifest
  External command Execute method and attributes
  Transaction mode
  Regeneration option
  Task dialogues for user messages
  Interactive filtered element selection
  Redesigned element filtering
  New element creation paradigm
  Access to pipe and conduit sizes

## Slide 59: Cable Tray Fitting Creation and Layout
Inserting a cable tray is as easy as a conduit, cf. p2c
Inserting fittings requires exact alignment, i.e. proper orientation

## Slide 60: Modeless Loose Connector Navigator
Filter for all MEP connectors in project
  Combine all relevant classes and family instance categories
Check IsConnected property on each connector
Unable to determine whether a wire is intended to be homerun
Log results to file and display it to user
Interactively navigate through results from a modeless dialogue
Ensure that modeless dialogue remains on top of Revit
Modeless navigation interacts with Idling event

## Slide 61: MEP Placeholder Sample
Placeholder ducts and pipes
  CreatePlaceholders and ConvertPlaceholders commands
Duct and pipe insulation and lining
  InsulateDuctwork command
Read and write access to MEP pipe settings and sizes
  GetPipeSettings command

## Slide 62: Summary and Further Reading

## Slide 63: Class Summary
Overview of the Revit MEP API
MEP API enhancements in recent releases of Revit
Working programmatically with Revit MEP models
Overview of available Revit MEP API samples

## Slide 64: Materials
Blog posts
  http://thebuildingcoder.typepad.com/mep
Autodesk University 2012 hand-out and sample code
  cp4108_rme_api.pdf
  cp4108_rme_api.zip
    HVAC and electrical MEP sample code – AdnRme.zip

## Slide 65: Learning More
Revit Developer Center: DevTV introduction, SDK, Samples, API Help
  http://www.autodesk.com/developrevit
Developer Guide and Online Help
  http://www.autodesk.com/revitapi-wikihelp
Public ADN Revit and Revit MEP API Webcasts, Trainings and Archives
  http://www.adskconsulting.com/adn/cs/api_course_sched.php > Revit API
  http://www.adskconsulting.com/adn/cs/api_course_webcast_archive.php > Revit API
Discussion Group
  http://discussion.autodesk.com > Revit Architecture > Revit API
API Training Classes
  http://www.autodesk.com/apitraining
ADN AEC DevBlog and The Building Coder Revit API Blog
  http://adndevblog.typepad.com/AEC
  http://thebuildingcoder.typepad.com
ADN, The Autodesk Developer Network
  http://www.autodesk.com/joinadn
DevHelp Online for ADN members
  http://adn.autodesk.com

## Slide 66
Autodesk is a registered trademark of Autodesk, Inc., and/or its subsidiaries and/or affiliates in the USA and/or other countries. All other brand names, product names, or trademarks belong to their respective holders. Autodesk reserves the right to alter product and services offerings, and specifications and pricing at any time without notice, and is not responsible for typographical or graphical errors that may appear in this document.