## Slide 1
Revit Structure API
Analysis Link, Rebar and Detailing
Jeremy Tammik
Developer Technical Services

## Slide 2: Prerequisite
Knowledge of Revit API basics
Introduction
Notes: This course assumes basic knowledge of Revit programming. We will not cover basics such as how to define an external command, add menus, use filtering, etc.

## Slide 3: Agenda
Recent Structural API Enhancements
  Revit Structure 2013
  Revit Structure 2014
Analysis Link
  Overview – workflow, rac versus rst, physical versus analytical model
  RstLabs – analysis link requirements and labs
  RstLink – sample analysis link application
Rebar
  Revit Structure rebar workflow
  Generate and extract rebar and its information
Detailing
  Generate views and sheets
  Import and export dwg and other external file formats
  Add text, dimensioning and annotation
Introduction
Notes: Our discussion here proceeds in three steps. First, look at the workflow and how it is supported by Revit Structure or RST. Secondly, walk through a series of labs related to extracting and analysing the data managed by RST. Finally, we will look at a sample application linking RST with an external application. In this case, the external stress analysis package is simulated by AutoCAD.

## Slide 4: Recent Structural API Enhancements

## Slide 5: Revit Structure 2013
Reinforcement
Welded Wire Mesh
Physical Properties
Structural Analytical Model
Analysis Visualization Framework
http://thebuildingcoder.typepad.com/blog/2012/06/the-revit-2013-structure-api.html

## Slide 6: Revit Structure 2014
Reinforcement API: area, path, fabric, fabric sheet, rebar, settings
Beam and Brace Parameters
Material Structural Asset
http://thebuildingcoder.typepad.com/blog/2013/04/whats-new-in-the-revit-2014-api.html

## Slide 7: Analysis Link Overview

## Slide 8: Completing the Building Information Model
  Building Information Modeling (BIM) – The creation and use of coordinated, internally consistent, computable information about a building project in design and construction
Image Courtesy of DDB Architectural International Ltd.
BUILDING
INFORMATION
MODELING
ARCHITECTS
STRUCTURAL
ENGINEERS
MEP SYSTEMS
ENGINEERS
BUILDERS
OWNERS
Focus
Overview
Notes: 8
Building information modeling (BIM) is the creation and use of coordinated, consistent, computable information about a building project in design that yields reliable digital representations of the building – representations used for design decision-making, production of high-quality construction documents, performance predictions, cost-estimating and construction planning, and, eventually, for managing and operating the facility. The focus of this presentation is on the structural part of it with Revit Structure.

## Slide 9: Revit Structure Target Projects
  Buildings -
  Any Type, any Size, any Complexity
  made of any kind of Materials
Overview
Notes: 9
Even if structural engineers can design any type of structures including bridges, tunnels, plants etc., RST focuses on building design. It does not mean that a user cannot design other type of structures, but the marketing that we do, the training and documentation materials that we provide are positioning RST on building design.

## Slide 10: Current Analysis Process
Overview
Notes: Currently, the analysis of a building involves a lot of manual data transfer with accompanying loss of information and additional cost. The aim of Revit and its building information model and Revit Structure and its linked physical and analytical model is to preserve more information, support communication between all parties involved, and reduce cost.

## Slide 11: Structural Market Definition
Designer
Structural
Analysis
Construction
Documentation
Engineer
Drafter
Design
User Types
Industry Tasks
Coordination
Contractor
Steel Detailer
Fabrication and
Shop Drawings
Fabrication
Overview
Notes: 11
The structural industry is extremely fragmented. We segment is into 2 parts: design and fabrication. The design is composed of 2 tasks (analysis and construction drawings) done by 3 actors and the fabrication focuses on shop drawings.

## Slide 12: Tasks and User Focus
Designer
Engineer
Drafter
Design
Revit Structure Focus
Construction
Documentation
Contractor
Steel Detailer
Fabrication and
Shop Drawings
Fabrication
Structural
Analysis
Modeling
Overview
Notes: 12
The focus that we have for RST is on the design part only where we do modeling for drawings and analysis. We do not do analysis.

## Slide 13: Issues to Address
Problems addressed by Revit Structure
  Same information is duplicated for different tasks
  Lack of coordination tools
    Between drafters and engineers
    Between architects and engineers
  Lack of standard software modelling platform
How are these problems addressed?
Overview

## Slide 14: Introduction
Overview
Notes: Revit Structure is used by a structural engineer to manage and combine data from several different sources:
Architectural data, the building design, which can come from Revit Architecture, but also from other Autodesk or non-Autodesk products.
Analysis data for stress analysis in external packages.
Details which are designed based on the analysis results.

## Slide 15: Structural BIM Workflow: The 4 Cs
ARCHITECTS
STRUCTURAL
ENGINEERS
BUILDERS
FABRICATORS
Coordination
Calculations
Construction Documents
Construction
Overview
Notes: 15
In the context of the structural BIM, we focus on four C’s which require significant coordination between architects, structural engineers, fabricators and builders:
Coordination
Calculations
Construction Documents
Construction
Developers and ADN partners can develop applications for each of the four Cs:
- Coordination with other disciplines
  Using the rich information in RST and process it against other disciplines
Calculations or Analysis
  Link analysis and design applications
Construction documentations
  Focus on local standards
  Automation
Construction
  Use the information downstream for fabrication

## Slide 16: Application Development Opportunities
Integration of analysis and design software
Automatic modeling
  Reinforcement
  Framing
  Connections (Steel, precast)
  Portal frames
  Bridge/tunnels
  Special structures (towers, retaining walls)
Data exchange (with other AutoCAD based applications)
Scheduling
Drawing automation
…
Overview
Notes: As the API is robust, there are many areas of opportunity to port existing applications to RST or to develop new ones.
The API is a great way to automate repetitive manual tasks such as reinforcement, framing modeling. There is also an opportunity to create dedicated Revit families and to drive their generation with the API such as steel connections. You can also imagine building wizard type applications that generate civil structures including soil, geometry reinforcement etc. The API is also built so you can link the RST model to your existing application and complete what RST does not do such as local standard drawings or schedules. With the API you can drive an application to generate a DWG file and then import it automatically in RST.
16

## Slide 17: Application Development Opportunities
Integration of analysis and design software
Automatic modeling
  Reinforcement
  Framing
  Connections (Steel, precast)
  Portal frames
  Bridge/tunnels
  Special structures (towers, retaining walls)
Data exchange (with other AutoCAD based applications)
Scheduling
Drawing automation
…
Overview
Notes: Today we will focus on the three highlighted areas.
17

## Slide 18: Comparison with Revit Architecture
  General User Interface
  Command organization
  Category filtering
  Functionality added
  Analytical model (generation and adjustment)
  Load modelling
  API specific model and load objects
  Rebar modelling
  Composite metal deck
  Graphical column schedule
  ...
Overview
Notes: Revit Architecture and Structure have a lot of common features. The differences are visible in the user interface in the command organisation and the category filtering. Some structure-specific functionality has been added.

## Slide 19: Comparison with Revit Architecture
  Functionality removed
  Reflected ceiling plans
  Room related functionalities
  Model text
  ...
Overview
Notes: Some functionality has also been removed.

## Slide 20: Analytical Model
Structural analysis model differs from drawing model
Revit Structure solves this problem
Physical model is used for drawings, coordination and construction
Analytical model is the simplified model used for analysis
Overview
Notes: The most important problem of the structural industry is the fact that the information used for structural analysis is physically different than the one used for drawings. Revit Structure solves this problem. The physical model is the model that we use for drawings, coordination and construction, and the analytical model is the simplified model used for analysis.
Some examples show the discrepancies between the analytical and physical models.
For example, consider a plan view where the walls need to be aligned for the analysis and the beams need to join the centre of columns to end of walls.
Another example is an elevation where the analytical model is horizontally projected even if the physical model of the beam has a slope.
Finally, consider a situation where the physical model of the beam is curved and the analytical model is segmented.
Revit Structure maintains the coordination between the 2 models and will keep the analytical model of each element connected.
As a third party analysis developer, you just need to work with the analytical model.
20

## Slide 21: What is in the analytical model?
Members that need to participate in the analysis
Geometry (location)
    Sections
    Materials
    Release conditions
    Reference to level (optional)
Loads
    Load cases
    Load combinations
    Point, line, area loads
Boundary conditions
    Support data
Overview
Notes: In this presentation, we explain how to access all this information.
21

## Slide 22: Analytical vs Physical Model
Overview
Notes: Revit Structure combines the physical model which drives the modeling and documentation process with the analytical model which drives the analysis process and export to third party analysis software.
The Revit Structure analytical model can be adjusted for analysis purposes while the physical model stays accurate for documentation.

## Slide 23: Analytical vs Physical Model
Overview
Notes: Here are examples of different cases highlighting the difference between the physical and the analytical models and the need for flexibility in linking the two:
The end points of two beams may are not at the same location. We want to the end points of their analytical models to be located at the same point. An engineer decides to move the end of one beam.
Remodelling an old historic building, walls may not be straight. An engineer decides to approximate them by planes for analysis.
Two walls with different thicknesses but aligned analytical planes.
A wall with a parapet that does not need to be included in the analysis.
Adjusting the location of analytical columns horizontally.
The cases are taken from AE_CD_RST2008/Analysis_workflows/Analysis_Workflows.pdf.

## Slide 24: Data Exchange Workflow
Geometry
Physical
Analytical
Loads
Connectivity
Material
Project parameters
Overview
Notes: In general, we start off with a physical model. This can be used to automatically generate the analytical one. The analytical model is exported to an external analysis package, which adds its own data. As a result of the analysis, the analytical model may be modified, resulting in changes in the physical model as well. New changes may be added in the physical model as well. All of these processes may continue over many iterations.
The example presented displays the following steps:
RST defines the physical model, analytical model composed of geometry, loads, connectivity (release and boundary conditions), material properties, project parameters. This is information is accessible via the API
In the analysis software we get the analytical model
Analytical model initializes specific properties not present in RST (here they are symbolized with X and Y) and the user can change them. We can do an analysis, delete specific members, change sections and then the analysis software updates the RST model
Changes can be add, delete, create, and move members and also add new properties to RST members
If we select a column and duplicate it, it will have the Y parameter that was defined in 3)
So the next time we round trip the data to the 3rd party, we retrieve the Y parameter.

## Slide 25: Analysis Requirements
  Extract the analytical model geometry
  Extract the load cases, load combinations, loads
  Extract release and boundary conditions
  Update the model with changes and new and deleted elements
  Add load cases and load combinations
  Add loads and reactions
  Add project information, shared parameters
  Add shared parameters on structural objects
Overview
Notes: Now we understand the structural workflow and its needs, we can start looking at the API features provided to address these needs.
Here is an overview of the typical requirements for implementing a link to an external analysis package using the RST API.
In the following slides, we will look at the Revit samples and a series of labs demonstrating how to address these issues one by one.
Finally, the results of these labs will be integrated into the sample link application.

## Slide 26: Adding local parameters to Revit
Shared parameters
  Can be defined in an external file
  Can be added with the API
  Can be defined per element
  Can be project specific, e.g. building codes
Templates
  Can contain specific information such as load combinations
Overview
Notes: Here are some different strategies for a third party application to add new properties in the database.
26

## Slide 27: Analytical model access
How to get the ...
  ... thickness of a wall with multiple layers?
    SDK sample TestWallThickness
  ... analytical model of an in-place family?
    SDK sample AnalyticalViewer
  ... analytical model defined in an external family?
    SDK sample AnalyticalViewer
  ... multiple analytical segments of a curved beam?
    Tessellate the underlying curve
Overview
Notes: Here are some typical frequently asked questions and examples on how to solve them.
27

## Slide 28: Useful Revit SDK Samples
Parameters
  BrowseBindings
  CreateShared
  FireRating
  InvisibleParam
Analytical Model
  AnalyticalSupportData_Info
  AnalyticalViewer
  BoundaryConditions
  Loads
  RotateFramingObjects
  SlabProperties
  SpanDirection
Overview
Notes: Currently, information on how to combine Revit API calls to achieve certain complex tasks is contained mainly in the SDK samples. Here is a list of some of the Revit SDK samples which address areas related to structure.

## Slide 29: Revit Structure Analysis Labs

## Slide 30: Revit Structure Analysis Labs
Loads
  1-1 Load cases, natures, combinations, usages
  1-2 Point, line and area loads
  1-3 Load parameters and modification
  1-4 Load symbols
  1-5 Creating load objects
Structure
  2-1 Columns
  2-2 Framing
  2-3 Foundations
  2-4 Structural standard family instances
  2-5 Structural system family instances: walls, floors, footings
Analytical Model
  3 Analytical model
RstLabs
Notes: In the section, we demonstrate step by step how to implement the functionality required for an application linking Revit Structure with an external analysis package. The first group of labs addresses access and modification of load data, the second examines the building structure, and the third addresses the entire analytical model.

## Slide 31: Load Grouping Objects
  Load Cases
  Load Natures
  Load Combinations
  Load Usages
  Lab 1-1
  To retrieve load case, nature, combination and usage objects, simply filter for the corresponding object class LoadCase, LoadNature, LoadCombination and LoadUsage
  To create new objects, use the Autodesk.Revit.Creation.Document methods NewLoadCase(), NewLoadCombination(), NewLoadNature(), NewLoadUsage() accessible through ActiveDocument.Create
RstLabs
Notes: This first lab extracts and lists the load cases, natures, combinations and usages defined in the Revit model.

## Slide 32: Loads Grouping Code
Retrieve objects
// load natures
IList<Element> ldNatures = RstUtils.GetInstanceOfClass( doc, typeof( LoadNature ) );
public static IList<Element> GetInstanceOfClass(
Document doc,
Type type )
{
FilteredElementCollector collector = new FilteredElementCollector( doc );
return collector.OfClass( type ).ToElements();
}
Create objects
        LoadCase.Create(document,string name, LoadNature nature, Category category );
        LoadNature.Create(document,string name)
        LoadUsage.Create(document,string name)
        LoadCombination.Create(document, string name,LoadCombinationType type,LoadCombinationState state)
RstLabs

## Slide 33: Loads Grouping Demo
RstLabs
Notes: Todo: add image of model.
To run the demo, install and compile RstLabs, add Lab 1-1 to Revit.ini, start Revit, and select the external command.
[ExternalCommands]
ECCount=1
ECName1=RS Lab1-1 Load Natures, Cases and Combinations
ECDescription1=Lab1_1...
ECClassName1=RSSolvedLabsCode.Lab1_1
ECAssembly1=C:\a\j\adn\rst\rst_api\RSSolvedLabsCode\bin\RSSolvedLabsCode.dll

## Slide 34: Access to Load Objects
  Point Loads
  Line Loads
  Area Loads
  Lab 1-2
  Shows how to access all load objects using the base or specific classes
  All three load classes are derived from LoadBase
  Creation through NewAreaLoad (3 overloads), NewLineLoad (2), NewPointLoad
RstLabs
Notes: Lab 1-2 shows how to access all load objects using the base or specific classes. All three load classes are derived from LoadBase. They are creation through AreaLoad.Create() (3 overloads), LineLoad.Create()(3 overloads), and PointLoad.Create()(3 overloads)

## Slide 35: Retrieve Load Objects
// get all loads
IList<Element> loads = RstUtils.GetInstanceOfClass( doc, typeof( LoadBase ), false );
/// <summary>
/// Return all instances of the specified class,including the derevided class instances.
/// </summary>
public static IList<Element> GetInstanceOfClass(
Document doc,
Type type,
bool bInverted )
{
FilteredElementCollector collector = new FilteredElementCollector( doc );
ElementClassFilter classFilter = new ElementClassFilter( type, bInverted );
return collector.WherePasses(classFilter).ToElements();
}
RstLabs
Notes: Just like in the preceding lab, we iterate over all Revit elements and pick out the object types of interest. For each load type object, a number of properties are defined for extracting and modifying data.

## Slide 36: Load Objects Demo
RstLabs
Notes: Todo: add image of model.
Open RstLabs.rvt to obtain a model with a few predefined loads.
Run the external command Lab 1-2 after adding RstLabs.dll to Revit.ini.

## Slide 37: Load Object Parameters
  Lab 1-3
  Shows more details about loads, this time from selected objects
  How to access load parameters
  How to modify load objects
        Dim iter As ElementSetIterator = doc.Selection.Elements.ForwardIterator
        While iter.MoveNext
        Dim elem As Revit.Element = iter.Current
        If TypeOf elem Is PointLoad Then
        ListAndModifyPointLoad(CType(elem, PointLoad))
        ElseIf TypeOf elem Is LineLoad Then
        ListAndModifyLineLoad(CType(elem, LineLoad), app)
        ElseIf TypeOf elem Is AreaLoad Then
        ListAndModifyAreaLoad(CType(elem, AreaLoad), app)
        End If
        End While
RstLabs
Notes: Lab 1-3 continues the exploration about loads.

## Slide 38: Get Parameter by Display Name
Direct parameter access by display name
        Parameter para = elem.get_Parameter( name );
Some parameters are accessible via display name only
Using BuiltInParameter enum is language independent
        elem.get_Parameter( BuiltInParameter.LOAD_IS_REACTION )
RstLabs
Notes: Some element parameters can be accessed via display name only. In general, we try to use the BuiltInParameter enum to access parameters whenever possible, since it is language independent.

## Slide 39: Point Load Parameters
Equivalent
LOAD_IS_REACTION "Is Reaction"
LOAD_CASE_ID "Load Case"
Similar
LOAD_USE_LOCAL_COORDINATE_SYSTEM "Orient to"
Built-in only
LOAD_USE_LOCAL_COORDINATE_SYSTEM_HOSTED
LOAD_IS_CREATED_BY_API
Display name only
"Fz"
RstLabs
Notes: Parameters vary from Revit version to version.

## Slide 40: Other Load Parameters
See list of 59 load-relevant built-in parameters at end of Labs1.vb
LOAD_ALL_NON_0_LOADS
LOAD_AREA_AREA
LOAD_AREA_FORCE_FX1
LOAD_AREA_FORCE_FX2
LOAD_AREA_FORCE_FX3
LOAD_AREA_FORCE_FY1
LOAD_AREA_FORCE_FY2
LOAD_AREA_FORCE_FY3
LOAD_AREA_FORCE_FZ1
LOAD_AREA_FORCE_FZ2
LOAD_AREA_FORCE_FZ3
LOAD_ARROW_SEPARATION
LOAD_ATTR_AREA_FORCE_SCALE_FACTOR
LOAD_ATTR_FORCE_ARROW_TYPE
LOAD_ATTR_FORCE_SCALE_FACTOR
LOAD_ATTR_LINEAR_FORCE_SCALE_FACTOR
LOAD_ATTR_MOMENT_ARROW_ARC
LOAD_ATTR_MOMENT_ARROW_LINE
LOAD_ATTR_MOMENT_SCALE_FACTOR
LOAD_CASE_CATEGORY
LOAD_CASE_ID
LOAD_CASE_NAME
LOAD_CASE_NATURE
LOAD_CASE_NATURE_TEXT
LOAD_CASE_NUMBER
LOAD_COMBINATION_FACTOR
LOAD_COMBINATION_NAME
LOAD_COMBINATION_STATE
LOAD_COMBINATION_TYPE
LOAD_COMMENTS
LOAD_COMMENT_TEXT
LOAD_DESCRIPTION
LOAD_FORCE_FX
LOAD_FORCE_FY
LOAD_FORCE_FZ
LOAD_IS_CREATED_BY_API
LOAD_IS_PROJECTED
LOAD_IS_REACTION
LOAD_IS_UNIFORM
LOAD_LINEAR_FORCE_FX1
LOAD_LINEAR_FORCE_FX2
LOAD_LINEAR_FORCE_FY1
LOAD_LINEAR_FORCE_FY2
LOAD_LINEAR_FORCE_FZ1
LOAD_LINEAR_FORCE_FZ2
LOAD_LINEAR_LENGTH
LOAD_MOMENT_MX
LOAD_MOMENT_MX1
LOAD_MOMENT_MX2
LOAD_MOMENT_MY
LOAD_MOMENT_MY1
LOAD_MOMENT_MY2
LOAD_MOMENT_MZ
LOAD_MOMENT_MZ1
LOAD_MOMENT_MZ2
LOAD_NATURE_NAME
LOAD_USAGE_NAME
RstLabs
LOAD_USE_LOCAL_COORDINATE_SYSTEM
LOAD_USE_LOCAL_COORDINATE_SYSTEM_HOSTED
Notes: Here is a full list of parameters relevant to loads given in the comment at the end of Labs1.vb.

## Slide 41: Point Load Properties
LoadBase
  HostElement
  LoadCaseName
  LoadCategoryName
  LoadNatureName
PointLoad
  Force
  Moment
  Point
Explore
  Help file
  Debugger
  RvtMgdDbg
  Reflection
RstLabs
Notes: Some of the values accessible through parameters are also exposed directly as properties on the object class.
Whenever you are looking for a specific property, you will need to explore the Revit API and one or more suitable sample models to determine what exactly you are looking for and how to access it.

## Slide 42: More Point Load Properties
RevitLookup
  Included in Revit SDK
RstLabs

## Slide 43: Modify Load Demo
// Scale Fz by factor 2
Parameter paramFz = ptLd.get_Parameter( "Fz" );
double Fz_old = paramFz.AsDouble();
paramFz.Set( 2.0 * Fz_old );
RstLabs
Notes: In "RS Labs.rvt", select a point, line and area load, then run the external command for Lab 1-3.

## Slide 44: Load Symbols
  Lab 1-4
  Retrieve load symbols aka types available in the project
  Determine load symbol family
    One utility for all load symbols (point, line and area)
    Another one specifically for point loads
  Load symbols are system families, not standard ones
RstLabs

## Slide 45: Retrieve Load Symbols
    Use filtered element access
    Pick out ElementType instances
    Check for structural loads category
    Make use of new classes LoadTypeBase, PointLoadType, LineLoadType, AreaLoadType
    Search for the base class instead of the category
IList<Element> types = RstUtils.GetInstanceOfClass(
doc, typeof( LoadTypeBase ), false );
/// <summary>
/// Return all instances of the specified class,including the derevided class instances.
/// </summary>
public static IList<Element> GetInstanceOfClass(
Document doc,
Type type,
bool bInverted )
{
FilteredElementCollector collector = new FilteredElementCollector( doc );
ElementClassFilter classFilter = new ElementClassFilter( type, bInverted );
return collector.WherePasses(classFilter).ToElements();
}
RstLabs

## Slide 46: Determine Load Symbol Family
  No dedicated classes
  Examine family name parameter
  BuiltInParameter.SYMBOL_FAMILY_NAME_PARAM equals “Point Loads”, “Line Loads”, “Area Loads”
RstLabs

## Slide 47: Creating Load Objects
  Lab 1-5
  Show how to create a new Load object, specifically PointLoad
    One as reaction, simulating analysis result
    One as standard external load
  Also show how to
    Set a selected symbol for this new load
    Assign the load to a selected load case
RstLabs
Notes: Lab 1-5 shows how to create a new load object, specifically a point load. It creates two new point loads by calling NewPointLoad() with somewhat arbitrary parameters. One as reaction, simulating an analysis result, the other is a standard external load. It also shows how to set a selected symbol for this new load and assign the load to a selected load case. To assign a selected symbol to it, all point load symbols in the document are retrieved and the user is allowed to select one of them. Its id is then assigned to the newly created point load ELEM_TYPE_PARAM. Similarly, to assign a load case, all load cases are retrieved and displayed and the selected one's id is assigned to the LOAD_CASE_ID parameter.

## Slide 48: Point Load Creation
Create
  PointLoad.Create( Document aDoc, AnalyticalModel host, XYZ forceVector, XYZ momentVector, PointLoadType symbol )
  PointLoad.Create( Document aDoc, AnalyticalModelStick host, AnalyticalElementSelector selector, XYZ forceVector, XYZ momentVector, PointLoadType symbol )
  PointLoad Create( Document aDoc, XYZ point, XYZ forceVector, XYZ momentVector, PointLoadType symbol, SketchPlane plane )
  Assign Symbol
  Iterate over all point load symbols
  Assign selected one’s id to parameter
        BuiltInParameter.ELEM_TYPE_PARAM
Assign Load Case
  Iterate over all load cases
  Assign selected one’s id to parameter
        BuiltInParameter.LOAD_CASE_ID
RstLabs

## Slide 49: Structure Load Creation
Load creation methods
  PointLoad Create( Document aDoc, XYZ point, XYZ forceVector, XYZ momentVector, PointLoadType symbol, SketchPlane plane )
Added a load type and sketch plane argument
  Optional, can be null (Nothing in VB) = Default load type
  Point (Line/Area) LoadType and *LoadTypeSet objects added
Supports creation of hosted loads
  Overloads for assignment of a host element or geometry reference of a host element to create the hosted loads
NewPointLoad(), NewLineLoad() and NewAreaLoad()
RstLabs
Notes: Revit Structure has enhanced load elements by adding their symbols. In the API, parameters used for load creation have changed: all load creation methods now take an optional load type and sketch plane argument. Both of these arguments are optional and can be supplied null (Nothing in VB) to use the default load type for the category of load being created.
Point(Line/Area)LoadType and Point(Line/Area)LoadTypeSet objects are added.
In addition, the Autodesk Revit API now supports creation of hosted loads. Several overloads have been added for NewPointLoad(), NewLineLoad() and NewAreaLoad() permitting assignment of a host element or geometry reference of a host element to create the hosted loads.

## Slide 50: Columns and Framing
  Structural Elements
  Standard families
  Lab 2-1, 2
  Retrieve all structural 'line segment' or 'stick' elements
    Columns belong to a separate standard family
    Others such as beam, brace, joist, etc. belong to the framing standard family
RstLabs
Notes: The next section explores accessing and modifying structural elements and their data in RST.

## Slide 51: Select all columns
  Select all standard family instances for category OST_StructuralColumns
BuiltInCategory bicSc = BuiltInCategory.OST_StructuralColumns;
List<Element> columns = RacUtils.GetAllStandardFamilyInstancesForACategory( app, bicSc );
. . .
public static IList<Element> GetAllStandardFamilyInstancesForACategory(
Document doc,
BuiltInCategory bic )
{
List<Element> elements = new List<Element>();
//The following commented code works for Revit 2010. Revit 2011 has new way to collect elements
FilteredElementCollector collector = new FilteredElementCollector( doc );
return collector.OfCategory( bic ).OfClass( typeof( FamilyInstance ) ).ToElements();
}
RstLabs
Notes: To select all columns in the model, we once again use filtering to select all standard family instances for category OST_StructuralColumns. We can display generic element and column properties such as element id, symbol name, structural type and analytical model type.

## Slide 52: Select all framing elements
  Select all standard family instances for category OST_StructuralFraming
//et all structural framing elements - similar to Lab 2-1:
BuiltInCategory bicSf = BuiltInCategory.OST_StructuralFraming;
IList<Element> frmEls = RacUtils.GetAllStandardFamilyInstancesForACategory( doc, bicSf );
string msg = "There are " + frmEls.Count.ToString() + " structural framing elements:";
foreach( FamilyInstance fi in frmEls )
{
msg += "\r\n " + RstUtils.StructuralElementDescription( fi );
}
public static string StructuralElementDescription( FamilyInstance e )
{
BuiltInCategory bic = BuiltInCategory.OST_StructuralFraming;
Category cat = e.Document.Settings.Categories.get_Item( bic );
bool hasCat = ( null != e.Category );
bool hasUsage = hasCat && e.Category.Id.Equals( cat.Id );
return e.Name
+ " Id=" + e.Id.IntegerValue.ToString()
+ ( hasCat ? ", Category=" + e.Category.Name : string.Empty )
+ ", Type=" + e.Symbol.Name
+ ( hasUsage ? ", Struct.Usage=" + e.StructuralUsage.ToString() : string.Empty ) // can throw exception "only Beam and Brace support Structural Usage!"
+ ", Struct.Type=" + e.StructuralType.ToString();
}
RstLabs

## Slide 53: Foundations
  Structural Elements
  Foundations standard family
  Lab 2-3, 4
  Retrieve structural foundation elements
    May not be needed for analysis package
  Alternative approach retrieves all standard family instances having structural usage, i.e., having an analytical model
RstLabs
Notes: Foundations are structural elements and also make use of a standard family. Lab 2-2 demonstrates how to retrieve all structural foundation elements. This may not be required for every analysis package. An alternative approach would be to retrieve all standard family instances having structural usage, i.e., having an analytical model.

## Slide 54: Retrieve Foundations
  Get all standard structural foundation elements
  Category OST_StructuralFoundation
  Excludes 'Wall Foundation' System Type under 'Structural Foundations' category in the Browser
    These belong to 'Continuous Footing' system family, Lab 2-3
  Excludes 'Foundation Slab' System Type under 'Structural Foundations' category in the Browser
    These are internally implemented as Revit 'Floor' system family, Lab 2-3
RstLabs
Notes: To retrieve all foundations in the model, we can use the same approach as above, getting all standard structural foundation elements, using the category OST_StructuralFoundation. This excludes the 'Wall Foundation' system type under 'Structural Foundations' category in the browser, because these belong to the 'Continuous Footing' system family, and also the 'Foundation Slab' system type under the 'Structural Foundations' category in the browser, which are internally implemented as Revit 'Floor' system family. These are examined in Lab 2-3.

## Slide 55: Retrieve Structural Family Instances
  Alternative approach
  Select all standard family instances with an analytical model
IList<Element> instances = null;
FilteredElementCollector collector = new FilteredElementCollector( doc );
instances = collector.OfClass( typeof( FamilyInstance ) ).ToElements();
string msg = "All structural family instances (generic check):";
foreach( FamilyInstance fi in instances )
{
// Note that instead of looping through and checking for a
// non-null analytical model, we might also be able to use some
// other criterion that can be fed straight into the Revit API
// filtering mechanism, such as structural usage:
if( null != fi.GetAnalyticalModel() )
{
msg += "\r\n " + RstUtils.StructuralElementDescription( fi );
}
}
RstLabs
Notes: As an alternative approach, we can also iterate over the document elements and select all FamilyInstance objects having an analytical model.

## Slide 56: Walls, Floors, Footings
  Structural Elements
  System families
  Wall, Floor (Slab), Continuous Footing
  Lab 2-5
  Retrieve structural elements from these system families
  Not all instances will have analytical model (user-definable!)
RstLabs
Notes: The structural elements walls, floors, and footings also all make use of system families, specifically Wall, Floor (Slab), and Continuous Footing, respectively. Lab 2-3 shows how to retrieve all structural elements from each of these system families. Please note that some instances may not have an analytical model, since this property is user definable.

## Slide 57: Analytical Model
  Abstract API base class
    AnalyticalModel
  Specific derived classes, gone in 2011
    Wall AnalyticalModelWall
    Floor AnalyticalModelFloor
    Cont.Footing AnalyticalModel3D
    Column, Framing AnalyticalModelFrame
    Foundation AnalyticalModelLocation
RstLabs
Notes: The analytical model makes use of a separate little class hierarchy derived from the abstract base class AnalyticalModel. It defines specialised derived classes for various structural elements.

## Slide 58: Retrieve Structural Walls
  Retrieve all Wall elements having an analytical model
/// <summary>
/// Return all structural walls in active document.
/// </summary>
public static List<Element> GetAllStructuralWalls( Document doc )
{
FilteredElementCollector collector = new FilteredElementCollector( doc );
collector.OfClass( typeof( Wall ) );
return new List<Element>(
from wall in collector
where null != wall.GetAnalyticalModel()
select wall );
}
  Same for ContFooting elements
RstLabs
Notes: To retrieve all Wall elements having an analytical model, we perform the normal Revit document elements iteration, pick out wall elements, and check for the presence of an analytical model using the Wall.AnalyticalModel property. The same approach can be used for ContFooting elements.

## Slide 59: Retrieve Structural Floors
  Retrieve all Floor elements having a non-empty analytical model
public static List<Element> GetAllStructuralFloors( Document doc)
{
FilteredElementCollector collector = new FilteredElementCollector( doc );
collector.OfClass( typeof( Floor ) );
AnalyticalModel am;
return new List<Element>(
from floor in collector
where ( null != ( am = floor.GetAnalyticalModel() )
&& ( 0 < am.GetCurves( AnalyticalCurveType.RawCurves ).Count ) )
select floor );
}
RstLabs
Notes: A similar approach as for walls can also be used for floor elements. However, in the case of floors, the analytical model may well be non-null, but still be empty, so we need to add an additional check that the number of curves in it, given by AnalyticalModelFloor.Curves.Size, is actually greater than zero.

## Slide 60: Analytical Model
  Investigate geometry contained in model
  Lab 3
  Retrieve detailed analytical model geometry for selected elements, depending on the family and/or category
RstLabs
Notes: Lab 3 implements some code to investigate the geometry contained in the analytical model. It retrieves detailed analytical model geometry for selected elements, depending on their family and/or category.

## Slide 61: Retrieve Analytical Model
Iterate over selected elements
  Wall
  Floor
  ContFooting
  FamilyInstance with category
    OST_StructuralColumns
    OST_StructuralFraming
    OST_StructuralFoundation
Get AnalyticalModel and list
  Curves
  Support data – cf. AnalyticalSupportData_Info SDK sample
RstLabs

## Slide 62: Retrieve Analytical Model
RstLabs

## Slide 63: Structural Analysis Link

## Slide 64: Structural Analysis Link
Introduction
Export and import
Practical examples
Sample application
RstLink
Notes: Now we have assembled all the tools we might need, let us put them together into an actual Revit Structure Analysis link application. First we discuss some general questions regarding applications linking Revit with external programs, followed by some practical examples.

## Slide 65: Analysis Link Introduction
There are MANY ways in which the link can be designed
There are MANY implementation scenarios concerning
  Which structural elements are passed between the applications
  Which kind of model changes are automatically supported in either of them
It is up to the particular 3rd party package and its implementer to design, code and document the link
  Revit Structure API provides the tools to do this
  RST does not pre-determine the design of the link application
RstLink
Notes: There are many different implementation scenarios in which it might be useful to link a Revit building model with some external data, both RST-specific for analysis as we are discussing here, and also generic for other situations. Obviously, there are also many ways in which such a link can be designed.
For the RST analysis link, we need to decide which structural elements are passed between the applications and what kind of model changes are automatically supported in either of them.
It is obviously up to the individual third party package and its implementer to design, code and document the link. The Revit Structure API provides the required tools to do this, and does not pre-determine the design of the link application in any way.

## Slide 66: Analysis Link Export
Data export from Revit to 3rd party A&D application
Use a custom Revit external command to export relevant data
  App's native file/DB format — typically proprietary
  App's neutral file/DB format — typically public
  Public neutral file/DB format supported by the app
  Intermediate file/DB format purpose-designed for the link
  ...
The choice depends on the combination of technical, functional, commercial and political requirements...
RstLink
Notes: For data export from Revit to a third party A&D application, one will generally use a custom Revit external command to export relevant data. The format used for this communication is once again completely up to the implementer, and could be any one of the following.

## Slide 67: Analysis Link Import
Define another custom Revit external command
The choice of options and reasoning is basically the same as for the export
The chosen file format need not be the same as for the export, though typically it would be
RstLink
Notes: For importing the updated and modified data from the external application back into Revit, one would generally define another custom Revit external command. The choice of options and reasoning is basically the same as for the export. The chosen file format does not need to be the same as for the export, though typically it would be.

## Slide 68: Practical Examples
RstLink
  Simple demonstration application
MidasLink
  Simple but real
FireRating
  Minimal generic Revit
RDBLink
  Generic Revit BIM, not RST specific
RstLink

## Slide 69: Practical Example
AutoCAD simulates A&D 3rd party app
  AutoCAD.NET API utilities used on the 'other' side
  Xdata used to store Revit Structure specific info on standard AutoCAD entities
  AutoCAD Dynamic Properties COM API used for the link-specific UI within AutoCAD
Intermediate, purpose designed XML
  Used in both directions
  For simplicity, based on .NET SOAP serialization
  Custom .NET neutral classes utilized by both sides' export/import commands
RstLink
Notes: We have implemented a custom designed practical example of a Revit Structure analysis link application called RstLink to accompany this presentation. We use AutoCAD 2008 with an AutoCAD.NET plug-in to simulate the external third party analysis and design application and extended entity data, also known as xdata, to store Revit Structure specific information on standard AutoCAD entities. We use the AutoCAD Dynamic Properties COM API and the Object Property Manager OPM for the link-specific user interface within AutoCAD.
AutoCAD.NET API utilities used on the 'other' side
Xdata used to store Revit Structure specific info on standard AutoCAD entities
AutoCAD Dynamic Properties COM API used for the link-specific UI within AutoCAD
The data exchange in both directions between the Revit model and the A&D simulation in AutoCAD is implemented using an intermediate, custom designed XML format. For simplicity, the XML format is based on .NET SOAP serialization. Some neutral custom .NET classes are utilised by both sides' export and import commands.
Used in both directions
For simplicity, based on .NET SOAP serialization
Custom .NET neutral classes utilized by both sides' export/import commands
Before running the demo, the following applications need to be present:
RstLink - helper dll shared by both acad and revit client
RSLinkRevitClient - command implementations
RSLinkRevitApp - external application
RSLinkAcadClient - AutoCAD client
RSLinkAcadClientDynProps - dynamic Revit properties for AutoCAD objects
Here are possible steps to run the demo:
Set up Revit.ini to load either the client or the external application or both.
Open or create a sample model in Revit Structure.
Run the export command. You are prompted for a file location. A dialogue box pops up, reporting the number of exported elements.
Start up AutoCAD and load the client and the dynamic property application.
This can be achieved automatically by setting up AutoCAD to start in the RVT sample directory and placing an acad.lsp file there containing:
(defun s::startup()
(command "_netload" "RSLinkAcadClient.dll")
(princ "\nAutoCAD RSLink client loaded.")
(arxload "RSLinkAcadClientDynProps.arx")
(princ "\nAutoCAD RSLink dynamic properties loaded.")
(princ)
)
If it does not load automatically, you can load it manually by calling
(load "C:/a/j/adn/revit/rst_api/RVT/acad.lsp")
with the appropriate full path, and then call
(s::startup).
The commands defined by the AutoCAD client are RSImport, RSExport and RSMakeMember.
Use RSImport to load the xml file just exported from Revit.
Modify some cross sections in the model using the OPM, simulating modifications made by the A&D application, and optionally RSMakeMember to add some new elements.
Use RSExport to write the model back out again.
Back in Revit, use the import command to read the modifications and update the Revit model accordingly. Dialogue boxes are displayed to report the number of elements imported and modified. Note that the column types were swapped. Currently, the new elements defined by RsMakeMember are ignored.

## Slide 70: RstLink Modules
RstLink
  Helper dll shared by both acad and revit client
RSLinkRevitClient
  Revit command implementations
  RSLinkImport, RSLinkExport
RSLinkRevitApp
  Revit external application
RSLinkAcadClient
  AutoCAD.NET client
  RSImport, RSExport, RSMakeMember
RSLinkAcadClientDynProps
  Dynamic Revit properties for AutoCAD objects
RstLink

## Slide 71: RstLink Revit Export
RstLink

## Slide 72: RstLink AutoCAD Import
Invoke RSImport command
RstLink

## Slide 73: Modify Cross Section
Edit dynamic properties
Change cross section
RstLink

## Slide 74: Add new Members and Data
Invoke RSMakeMember command
RstLink

## Slide 75: Import Modified Data into RST
RSExport from AutoCAD
Import into Revit
  Column type was swapped
  New elements are ignored
RstLink

## Slide 76: Another Practical Example
MidasLink
Subscription only module
Old source code available on ADN, but no update
Search for "MidasLink"
  http://adn.autodesk.com/adn/servlet/item?siteID=4814862&id=9628885&linkID=4901650
Includes
  Analysis package executable
  Documentation
  Source code
  Installer
RstLink
Notes: MidasLink is a Revit Structure add-in program that exports and imports the Revit model to and from the MIDAS/Gen structure analysis application. The source code is provided to help developers integrating analysis programs with Revit Structure. The compiled add-in is available to Revit Structure subscription customers.

## Slide 77: Analysis Software
ADAPT
  www.adaptsoft.com/releases.php
RISA
  www.risatech.com/partner/revit_structure.asp
RAM
  www.bentley.com/structural
CSC
MIDAS – MidasLink subscription module
Autodesk ROBOBAT
  http://www.extensions4revit.com/n/e4r
Complete updated list in the developer guide
  Section 29.4 Analysis Link
Analysis Partners site
  http://usa.autodesk.com/adsk/servlet/item?id=8447050&siteID=123112
RstLink
Notes: Here is an overview of some other available analysis link packages. An up-to-date list is available on the analysis partners site. Robot Millennium is an analysis software by Robobat, which is recently acquired by Autodesk.

## Slide 78: Rebar
Sample and API feature walkthrough in the rebar and detailing workflow context

## Slide 79: Revit Structure Rebar Workflow
Revit Structure 3D
Object Model
Physical Model
Analytical Model
3D Rebar Model
User
Input
3rd Party
Analysis
Design
Concrete Drawings
Specific Rebar Details
Specific Rebar Details
Shop
Drawing
Typical Rebar Details
3D Design
QTO
User
Input
User
Input
Manual
Automated
Rebar
Notes: Working with reinforcements in Revit Structure involves two phases. The initial phase is the building analysis, which may result in design changes. In the second phase, reinforcements are added, analysed, and detailed. Both phases may include multiple iterations. Many of the tasks required can be automated. This is where our applications can save a lot of time, effort, and eliminate sources for errors.
The central hub is the Revit Structure three-dimensional object model which integrates the physical and analytical models used respectively for the building design and analysis. The 3D rebar model is integrated in this database. The physical model is used to generate concrete drawings including rebar specific details. The rebar model can be used to generate rebar specific details and quantity takeoffs. The analytical model is used to connect to third party analysis and design packages, which in turn can help define the rebar model.

## Slide 80: The 3D Rebar Model
Revit Structure has a 3D rebar model composed of
  Single bars
  Sets (array of bars with rules)
  Area reinforcement for slabs and walls
  Path reinforcement for slabs
3D rebar model can be generated
  Manually by user
  Loaded from a group that defines a cage
  Generated with the API from analysis and design software or from macros
Advantages of 3D rebar model
  Quantities
  Complex layout
  Automatic reinforcement drawings
  Basic scheduling
Scheduling is specific to each country
  Opportunity for third party developers to use the 3D rebar model to generate DWG schedules and import them back as a drafting view in Revit Structure
Rebar
Notes: 80

## Slide 81: Relationship Between Topics
Rebar
  Generate rebar and define rebar shape
  Extract rebar information
Truss
Detailing
  Generate a section view
  Generate a drafting view
  Create a sheet
  Import and export external file formats (e.g., dwg)
  Add text, dimensioning and annotations
Rebar
Notes: Here are some relationships between these rebar topics and the rebar workflow: after the structural framing analysis part is done, an engineer will take the values of the load and stress information for each element and design the rebar for each element. You design the size of the column, number of rebars, and number of rib-bars. Based on this information, a rebar can be generated externally. It may need modification, which requires extraction and analysis of existing information. The extracted information may also be used for estimation purposes. To show the rebar placement in a column or beam, you need a section view. The Revit SDK samples CreateSimpleAreaRein and CreateComplexAreaRein generate reinforcement elements, and can be used to demonstrate the kinds of section view required. For structure detailing, we need a drafting view where we may want to import a dwg file. Adding text, annotations and dimensioning is further typical detailing functionality. Some of the items listed here are general, but especially useful as part of the rebar workflow for structural detailing. The underlined topics are new or updated in Revit 2009.

## Slide 82: Generate Beam or Column Rebar
Sample: Reinforcement
  Create reinforcement bars in selected non-reinforced concrete beam or column
  Beam rebar: top, bottom or transverse
  Column rebar: transverse or vertical
Class
    Autodesk.Revit.Elements.Rebar
Methods
Rebar
// two overloaded functions in 2009
Rebar r = doc.Create.NewRebar( RebarStyle.Standard, rebarType, startHook, endHook,
m_hostObject, normal, curves, (int)startOrient, (int)endOrient, false, true );
r = doc.Create.NewRebar( barShape, barType, m_rebarHost, origin, xVec, yVec );
//Revit 2012, 2013, 2014. The create methods are in Rebar class.
// Invoke the NewRebar() method to create rebar
Rebar createdRebar = Rebar.CreateFromCurves(m_revitDoc, Autodesk.Revit.DB.Structure.RebarStyle.Standard, rebarType, startHook, endHook,
m_hostObject, normal, curves,startOrient, endOrient, false, true);
Notes: We can use the Revit SDK sample Reinforcement to demonstrate the creation of new reinforcement elements. It creates a bar set in a selected concrete beam or column element that does not have any reinforcement. Three kinds of beam rebar are created: top, bottom and transverse rebar. Two kinds of column rebar are created: transverse and vertical. It uses the Autodesk.Revit.Creation.Document.NewRebar() method to create rebar for the selected host. The NewRebar() method expects two parameters RebarBarType and RebarHookType. Suitable values for these two parameters can be retrieved by iterating the active document elements.
[MH] This sample shows how to create Rebar in concrete element (Beam or Column) which does not have any reinforcement. The method used to create Rebar, Create.NewRebar, has been changed in 2009. The first argument RebarStyle.Standard is an enumeration value – you can choose either standard/stirrupTie (stirrup or tie bar). The style affects the bend radius and the set of allowable hooks. It also affects the rebar instance auto-constraining behavior. …

## Slide 83: Reinforcement Implementation
FrameReinMakerFactory class manages all the work
  Precondition checks
    Is the selected object a beam or column?
    Is it made of concrete?
    Does it already contain any rebar elements?
  Create a corresponding FrameReinMaker and the reinforcement rebars
Host-dependant working classes
  BeamFramReinMaker and ColumnFramReinMaker
GeomUtil
  Basic geometric utility methods
GeometrySupport
  Base class for BeamGeometrySupport and ColumnGeometrySupport, manages the solid of beam or column, the extend or sweep path of the beam or column, the beam or column direction vector, lists to store the edges and points, the transformation etc.
ParameterUtil
  Utility methods find or set certain parameter
Rebar

## Slide 84: Generate Rebar Demo
Ensure only one beam or column is selected
Retrieve all rebar types and all hook types
Retrieve and analyse member geometry
Run worker method
Rebar
Notes: This is demonstrated by the sample Reinforcement. The sample can create rebar for both beam and column.
Register the command:
[ExternalCommands]
ECCount = 16
ECName16=Rebar - Reinforcement
ECClassName16 = Revit.SDK.Samples.Reinforcement.CS.Command
ECAssembly16 = C:\a\lib\revit\2021\sdk\Samples\Reinforcement\CS\bin\Debug\Reinforcement.dll
ECDescription16 = Create bar set in a selected concrete element (beam or column) that does not have any reinforcement.
Draw a Concrete Beam or Column elements without any reinforcement and select it.
Please make sure the beam or column section size is big enough, e.g. for column it can be 24x32.
Run the command.
Set the parameters for the rebar in the pop up dialog.
Click Ok, Rebar for the selected element (Beam or Column) will be created.
If you want to debug, this can be done from SDKSamples10.0.sln.

## Slide 85: Rebar API Enhancement in 2019
    Rebar is an instance of RebarShape
Added
    Autodesk.Revit.DB.Structure.RebarShape– topological layout of rebar
    Autodesk.Revit.DB.Structure.RebarShapeDefinition(ByArc/BySegments) – helper class to define RebarShape
    Autodesk.Revit.DB.Structure.RebarCoverType– rebar cover setting, name and value pair
    Autodesk.Revit.DB.Structure.RebarHostData– helper class to access to a host cover setting
    Samples: NewRebar
Rebar
Notes: RebarHostData and RebarCoverType: Clear cover is now associated with individual faces of valid rebar hosts. Access to the cover settings of a host is through the Autodesk.Revit.DB.Structure.RebarHostData object. A simpler, less powerful mechanism for accessing the same settings is provided through parameters. Cover is defined by a named offset distance, modeled as an element Autodesk.Revit.DB.Structure.RebarCoverType

## Slide 86: NewRebar Sample
Rebar
  Create a Rebar
  Define a custom Rebar shape

## Slide 87: NewRebar Sample (cont.)
Rebar
  Instructions under NewRebar/CS/Customize RebarShapes Step by step
Arc with radius(*)
(*) known issues – places rebar out side of a host objects both in UI and API
Collection of straight segments
Arc with chord length (*)
Lapped circle (*)

## Slide 88: NewRebar Sample (cont.)
Rebar
  RebarShapeDefinitionBySegments
  Create a RebarShape RebarShape myShape=RebarShape.Create()
  Create a RebarShapeDef RebarShapeDefinitionBySegments myDef = new RebarShapeDefinitionBySegments(doc,SegmentCount);
  Add shared parameters by external def myDef.AddParamater( externalDef, value )
  Add constraints to shape definition myDef.AddConstraintToSegment myDef.AddConstraintParallelToSegment myDef.AddBendDefaultRadius myDef.SetSegmentFixedDirection myDef.AddListingDimentionBendToBend
Notes: ExternalDefinition The parameter. To obtain this object, the following calls are required: Application.OpenSharedParameterFile(); Parameters.DefinitionFile.Groups.get_Item() or .create(); and Parameters.DefinitionGroup.Definitions.get_Item() or .create().

## Slide 89: Generate Floor or Wall Rebar
Sample: NewPathReinforcement
  Create path reinforcement
Class
    Autodesk.Revit.DB.Structure.Rebar
Method
Rebar
XYZ p1, p2; Line curve;
CurveArray curves = new CurveArray();
for( int i = 0; i < points.Count - 1; ++i )
{
p1 = new XYZ( points[i].X, points[i].Y, points[i].Z );
p2 = new XYZ( points[i + 1].X, points[i + 1].Y, points[i + 1].Z );
curve = Line.CreateBound(p1, p2);
curves.Append( curve );
}
// type is no longer needed, default is used in 2009:
return PathReinforcement.Create( Document document, Element hostElement, IList<Curve> curveArray, bool flip, ElementId pathReinforcementTypeId, ElementId rebarBarTypeId, ElementId startRebarHookTypeId, ElementId endRebarHookTypeId )
Notes: We can use the Revit SDK sample NewPathReinforcement to demonstrate how to create a new PathReinforcement element through the API. The PathReinforcement host is a floor or a wall. The method used is
PathReinforcement.Create( Document document, Element hostElement, IList<Curve> curveArray, bool flip, ElementId pathReinforcementTypeId, ElementId rebarBarTypeId, ElementId startRebarHookTypeId, ElementId endRebarHookTypeId );
We can use PathReinforcementType.Create() method to create a PathReinforcementType if there is none in current document. The Element argument is the host of the PathReinforcement. The CurveArray stores its path. The Boolean value indicates which side of the path the PathReinforcement is located on.
To run the sample, draw a Structure wall or slab, select it, and run this command. Draw the path of PathReinforcement you want to create. You can click right mouse button to finish drawing. Click the “Preview” button to preview the path reinforcement to be created. Select or unselect the “Flip” check box to create the PathReinforcement on the left or right side of the path. Click the “Create” button to create the PathReinforcement. You can clean and redraw the sketch of the path using the “Clean” button. Here is the central code snippet given an array of points defining the path.

## Slide 90: Extract Rebar Information
AreaReinParameters Sample
  Provides starting point
  Extended to list rebar information
  Uses built-in parameters
BarDescriptions Sample
  AreaReinforcement has a BarDescription property
  Same functionality as above
Generic Tools
  BuiltInParameterChecker
  RvtMgdDbg
Rebar
Notes: All the generic data extraction and debugging utilities such as RvtMgdDbg and BuiltInParameterChecker can be used to read parameters and other information from a rebar element.
In addition, the Revit SDK sample AreaReinParameters shows how to use the API to display and modify AreaReinforcement parameters. We have expanded the sample to list rebar elements and their parameters as well in a separate command RebarParas. The enhanced sample is included in the presentation material.
Another sample for extracting rebar information is the BarDescriptions sample. It shows how to find all BarDescriptions in the project, display their properties in a DataGridView, and export their parameter information to an external comma delimited *.csv file. BarDescription is a property of an AreaReinforcement element, so some AreaReinforcement elements should be drawn first.
Some rebar information is accessible through built-in parameters and can be determined using BuiltInParameterChecker, some is accessible only through hard-coded localised parameter names. The AreaReinParameters sample only works with floor or wall area reinforcements, not with rebar. Not all rebar parameters are accessible as built-in parameters. We can however retrieve almost all necessary information with its instance parameters, hence the RebarParas enhancement.

## Slide 91: Rebar Information Demo
Rebar
Notes: Register the command:
[ExternalCommands]
ECName32 = RebarParas
ECClassName32 = Revit.SDK.Samples.AreaReinParameters.CS.RebarParas
ECAssembly32 = C:\Revit\SDK\Samples\AreaReinParameters\CS\bin\Debug\AreaReinParameters.dll
ECDescription32 = Show parameters of a rebar
Select a rebar.
Run this command.

## Slide 92: Truss

## Slide 93: Truss
  RST, C#
  Create a truss of a selected truss type
  Change beam types
  Edit the profile of the truss
Truss

## Slide 94: Detailing

## Slide 95: Detailing
Detailing
  Generate a section view
  Generate a drafting view
  Create a sheet
  Import and export external file formats, e.g. dwg
  Add text, dimensioning and annotations
Enhanced Revit SDK samples
Detailing

## Slide 96: Generate Section View
Demonstrate creation of a Detail View
  Using NewViewSection()
  Creates detail view across the midpoint of selected element
  Works on linear elements such as slab, wall and beam
Create and initialise a bounding box
Detailing
// create a BoundingBoxXYZ and set the Max and Min properties:
BoundingBoxXYZ m_box = new BoundingBoxXYZ();
m_box.Enabled = true;
m_box.Max = new XYZ(LENGTH, LENGTH, 0);
m_box.Min = new XYZ(-LENGTH, -LENGTH, -HEIGHT);
// setting the Transform property is the most important thing.
// it defines the origin and the directions RightDirection,
// UpDirection and ViewDirection) of the created view:
Transform transform = GenerateTransform();
if (null == transform)
{
return false;
}
m_box.Transform = transform;
// Create a section view, pass the bounding box.
ViewSection section = ViewSection.CreateDetail(m_project.Document, DetailViewId, m_box);
Notes: The Revit SDK sample CreateViewSection demonstrates the creation of a detail view. Given a linear element such as a wall, floor or beam, it generates a section view across the midpoint of the element using the NewViewSection() method. It performs the following steps:
Retrieve the selected linear element
Generate a BoundingBoxXYZ instance to be used in NewViewSection()
Set its Max and Min properties
Generate a Transform instance for the BoundingBoxXYZ Transform property, which defines the origin and directions of the created view, including RightDirection, UpDirection and ViewDirection
Create the section view using the BoundingBoxXYZ.
The NewViewSection method takes a parameter of type BoundingBoxXYZ. The key part of the code is actually to create the box. And the key part for the box is to create its transform matrix. The actual matrix generated depends on the selected element type. Separate implementations are provided for beam, floor and wall. These are called from within GenerateTransform().

## Slide 97: Generate Section View Demo
Detailing
Notes: Use the Revit SDK sample CreateViewSection to demonstrate this.
Register the command:
ECName19=Rebar - CreateViewSection
ECClassName19=Revit.SDK.Samples.CreateViewSection.CS.Command
ECAssembly19=C:\a\lib\revit\2021\sdk\Samples\CreateViewSection\CS\bin\Debug\CreateViewSection.dll
ECDescription19=Create a section view across the mid point of the selected wall, floor or beam
Launch Revit 2021.
Open the project Rebar.rvt.
Select a beam or column with rebar.
Execute the external command.
Note that a new section view is added to the detail views in the project explorer.

## Slide 98: Generate Drafting View
Code
    Document doc = commandData.Application.ActiveDocument;
    // Create a drafting view
    ViewDrafting VD = ViewDrafting.Create();
Detailing
Notes: ViewDrafting.Create() method takes 2 parameters. We have added a second external command CreateDraftingView to the Revit SDK sample CreateViewSection to demonstrate this.

## Slide 99: Import DWG
Import
Detailing
DWGImportOptions opts = new DWGImportOptions();
opts.Placement = ImportPlacement.Centered; // Origin, Center, Shared
// other possible options.
opts.ColorMode = ImportColorMode.Preserved; // BlackAndWhite, Inverted, Preserved
//opts.CustomScale = 1;
opts.OrientToView = true; // true or false
opts.ThisViewOnly = false; // imports dwg, dgn, and dxf into active view only?
opts.Unit = ImportUnit.Default;
opts.View = m_revitApp.ActiveDocument.ActiveView;
opts.VisibleLayersOnly = false; // true or false
Revit.Element newElement = new Revit.Element();
rvtDoc.Import( dbox.FileName, opts,View,out newElement );
Notes: Importing and exporting DWG files is demonstrated by the Revit SDK sample ImportExportDWG. It shows how to export the current project to dwg files and import a dwg file into Revit. It also demonstrates how to and provides a user interface to set up the import and export options appropriately. To run it, start up Revit, open a suitable project, and execute the command.
To export, check the radio button “Export”. In the next dialog, specify the file name to export as, set the common options and click the “Option…” button to set the lower priority options; click the “Select…” button to select multi-views to export. Then click the “Save” button to perform the export.
To import, check the radio button “Import”. In the next dialog, specify the file to import from and set the other options. Then click the “Open” button to perform the import.
  The last parameter of the Import() method is an element. It is not neccessary to create a new element prior calling the Import() method. You can simply pass a variable of type Element and it can be null. This provides a possibility to return the element that was just imported, so that it can be accessed and modified after the import. For example, if you import an image, the import method gives you no scaling nor rotating options. If you would need this functionality, you can achieve it by manipulating the image after the import.

## Slide 100: Export DWG
Export
Detailing
opts dwgExportOptions = new DWGExportOptions();
opts.ExportingAreas = false; // export room and areas
opts.FileVersion = ACADVersion.R2018; // acad file version
opts.LayerMapping = “AIA”; // layer standard: AIA/CP83/BS1192/ISO13567
opts.LineScaling = LineScaling.ModelSpace; // or PaperSpace/ViewScale
opts.MergedViews = true;
opts.PropOverrides = PropOverrideMode.NewLayer; // or ByLayer/ByEntity
opts.SharedCoords = true;
opts.TargetUnit = ExportUnit.Millimeter;
opts.ExportOfSolids = SolidGeometry.ACIS;
exported = rvtDoc.Export( folder, name, views, opts );

## Slide 101: Import and Export Demo
Detailing

## Slide 102: ImportExport
  All, C#
  ImportExportDWG was enhanced to handle additional file formats
    Export - dwg, 2D and 3D dwf and dwfx, gbxml and FBX
    Import - dwg and image file
    New API classes added
Detailing

## Slide 103: Create New dimensioning
Create a dimension between two references
CreateDimensions sample
Detailing
XYZ p1 = newLine.GetEndPoint(0);
p1.X += 5;
p1.Y += 5;
XYZ p2 = newLine. GetEndPoint(1);
p2.X += 5;
p2.Y += 5;
Line newLine2 = Line.CreateBound( p1,p2);
// set the references
. . .
// create a dimention
Dimension newDimension = rvtDoc.Create.NewDimension(
rvtDoc.ActiveView, newLine2, referenceArray );
Notes: New dimenioning can be generated through the API using the NewDimension() method. Searching globally through all the samples discovers one single instance of this method, in the CreateDimensions sample. This sample adds a command taking a selection of basic structural walls and adds dimensioning from the start to the end of each. Dimensioning is created between graphical references stored in a ReferenceArray instance. The key part is the creation of the reference array. Once the reference array has been set up, the creation of the dimensioning is simple.

## Slide 104: Dimensioning Reference Array
Create a reference array for a structural wall
Detailing
ReferenceArray referenceArray = new ReferenceArray();
Options options = rvtApp.Create.NewGeometryOptions();
options.ComputeReferences = true;
options.View = rvtDoc.ActiveView;
GeometryElement geomElem = wallTemp.get_Geometry(options);
foreach(GeometryObject geoObject in geomElem)
{
Curve curve = geoObject as Curve;
if (null != curve)
{
//find the two upright lines beside the line
if (Validata(newLine, curve as Line))
{
referenceArray.Append(curve.Reference);
}
if (2 == referenceArray.Size)
{
break;
}
}
}
Notes: For the basic wall, the location line of the wall is used to discover the two vertical edges at each end of one side of the wall. Some calculation and comparison work needs to be done in order to find the two right reference lines. For each of these two curves, a reference is added to the reference array. Note that the geometry options for obtaining the wall geometry have options.ComputeReferences set to true.

## Slide 105: Dimension Creation Tips
Extend the sample to work with other elements than structural wall
Architectural wall cannot get reference from edge
Use face instead - not all geometry has reference
Detailing
Solid solid = geoObject as Solid;
if(null != solid)
{
  FaceArrayIterator faceItor = solid.Faces.ForwardIterator();
  while (faceItor.MoveNext())
  {
    PlanarFace face = faceItor.Current as PlanarFace;
    if (null != face)
    {
      // find the two upright lines beside the line.
      // NOTE: overloading this function. We pick up the face in term of its Normal.
      if (Validata(newLine, face.Normal))
      {
      referenceArray.Append(face.Reference);
      }
      if (2 == referenceArray.Size)
      {
      break;
      // . . .

## Slide 106: Rebar dimensioning
Extending the sample to work with rebar
Need to dig into geometry elements ...
SPR #125909 API wish: create dimension between a column edge and a rebar center
Detailing
// get rebar reference
if (m_rebar != null)
{
GeometryElement gelement = m_rebar.get_Geometry(options);
foreach(GeometryObject geoObject in gelement)
{
Line line = geoObject as Line;
if (line != null && line.Reference != null)
{
referenceArray.Append(line.Reference);
}
}
}

## Slide 107: Add Tags
Simple Tag sample in RvtMgdDbg’s Test Framework
Detailing
if( elem is Rebar )
{
// Cast to Rebar and get its first curve
Revit.Elements.Rebar rebar = elem as Rebar;
Revit.Geometry.Curve curve = rebar. GetCenterlineCurves().get_Item(0);
// Create a rebar tag at the first end point of the first curve
IndependentTag tag = IndependentTag Create( Document document, ElementId symId, ElementId ownerDBViewId, Reference referenceToTag, bool addLeader, TagOrientation tagOrientation, XYZ pnt )
Notes: The NewTag method signature and its parameters:
public IndependentTag Create( Document document, ElementId symId, ElementId ownerDBViewId, Reference referenceToTag, bool addLeader, TagOrientation tagOrientation, XYZ pnt );
Parameters
Document
Type: Autodesk.Revit.DB Document The document to which the tag will be added.
symId
Type: Autodesk.Revit.DB ElementId The id for the FamilySymbol which determines the tag's type.
ownerDBViewId
Type: Autodesk.Revit.DB ElementId The view in which the tag will be visible.
referenceToTag
Type: Autodesk.Revit.DB Reference The host reference of the tag.
The reference can be to an element or subelement in a local or linked document.
addLeader
Type: System Boolean When true, the tag will be created with a straight leader with an attached end.
tagOrientation
Type: Autodesk.Revit.DB TagOrientation The orientation of the tag's head.
Pnt
Type: Autodesk.Revit.DB XYZ For tags without leaders, this point is the position of the tag head. For tags with leaders, this point is the end point of the leader, and a leader of default length will be created from this point to the tag head.

## Slide 108: Add Text
Detailing
if( elem is Rebar )
{
// cast to Rebar and get its first curve
Autodesk.Revit.DB.Structure.Rebar rebar = elem as Autodesk.Revit.DB.Structure.Rebar;
IList<Curve> curves = rebar.GetCenterlineCurves(false,false,false,MultiplanarOption.IncludeAllMultiplanarCurves,barPositionIndex);
Curve curve = curves[0];
// calculate arguments
XYZ origin = curve.GetEndPoint(0);
origin.X = curve.Length * 10;
XYZ baseVec = new XYZ(1, 0, 0);
XYZ upVec = new XYZ(0, 0, 1);
double textSize = curve.Length / 10;
double lineWidth = curve.Length / 50;
string strText = "This is " + rebar.Category.Name + " : " + rebar.Name
// create the text
Autodesk.Revit.DB.TextNote text = TextNote.Create(document, ElementId viewId, XYZ position, double width, string text, TextNoteOptions options); text.Width = curve.Length * 10; // set the width of the text
}
Notes: public TextNote.Create( Document document, ElementId viewId, XYZ position, double width, string text, TextNoteOptions options )
Parameters
Document
Type: Autodesk.Revit.DB Document A valid Revit document that is currently modifiable (i.e. with an open transaction).
viewId
Type: Autodesk.Revit.DB ElementId Id of the graphic view in which the note is to be created.
Position
Type: Autodesk.Revit.DB XYZ A model position of the new note.Note that the position's relation to the text's bounding box depends on the requested text alignment (set via the Options argument). It will be the box' top-left corner for a left-aligned text, the top-right corner for a right-aligned text, and middle-top point if the text is to be centered.
Width
Type: System Double Width [ft] of the text in paper space (i.e. as it is measured when printed.) If a line of text is longer than the given specified Width, the text will be automatically wrapped. If a a zero Width is supplied then this method will create an unwrapped text note element
Text
Type: System String Text to populate the text note with.
Options
Type: Autodesk.Revit.DB TextNoteOptions Options to control behavior and appearance of the text note.

## Slide 109: Thank you very much!
Thank you for your interest and attention!

## Slide 110
Autodesk is a registered trademark of Autodesk, Inc., and/or its subsidiaries and/or affiliates in the USA and/or other countries. All other brand names, product names, or trademarks belong to their respective holders. Autodesk reserves the right to alter product and services offerings, and specifications and pricing at any time without notice, and is not responsible for typographical or graphical errors that may appear in this document.